## Slide 1: Weekly
Delivery item 1：
  analysis with radix16 vgpr consumption for size 4096
    JIRA：Analyze and improve butterfly performance
    Dump info :
      rocprof -i input.txt -d ./ ./rocfft_test
      rpl_data_201112_014912_64111/input1_results_201112_014912/results.txt
    1d c2c 4096len kernel:
      fft_fwd_op_len4096
      group size = 256 (4 wave)
      lds = 4096DW (4 group per CU at most, 4 wave per SIMD)
      VGPR = 68 (3 wave per SIMD, 3 group per CU at most)
    If launch 4 group per CU
      Batch = 4 * CU_NUM
      Only 3 group inflight
      12 wave inflight per CU

## Slide 2: Weekly
Delivery item 1：
  Analysis vgpr usage for all size in the JIRA
    LDS: 16K DW per CU
    VGPR: 16K DW per SIMD, 64 thread per WAVE, 256 VGPR per thread
length | radix | VGPR | LDS(DW) | grp_size/ Wave | grp_lmt_lds (CU) | wv_lmt_vgpr (SIMD) | gpr_lmt_vgpr (CU) | Best Vgpr usage / (reduce) / group num
112 | 7 | 68 | 896 | 64 / 1 | 18 | 3 | 12 | 51 (17) / 20
512 | 8 | 40 | 512 | 64 / 1 | 32 | 6 | 24 | 32 (8) / 32
2187 | 3 | 48 | 2187 | 243 / 4 | 7 | 5 | 5 | 36 (12) / 7
3125 | 5 | 120 | 3125 | 128 / 2 | 5 | 2 | 4 | 84 (35) / 6
4096 | 16 | 68 | 4096 | 256 / 4 | 4 | 3 | 3 | 64 (4) / 4

## Slide 3: Weekly
Why compiler use 68 vgprs
  Input load and result write has the same address calculation in the beginning and end of the kernel
    addr_in = inOffset + ( 0 + me*1 + 0 + instr_step ) * stride_in; x16
    addr_out = outOffset + ( 0 + me*1 + 0 + instr_step ) * stride_out; x16
  Compiler will reserve some vgpr (about 16 vgprs) to hold the template variable, and allocate new vgprs to do global load
    temp_var = ( 0 + me*1 + 0 + instr_step)
reason

## Slide 4: Weekly
reason
Notes: __constant

## Slide 5: Weekly
  Example V8
    V8 (= me * 1 ) are allocate in the beginning of the kernel
      V8 = 0 + me * 1 + 0;
      S[4:5] = stride_in
      V[6:7] = (0 + me*1 + 0) * stride_in
      S[2:3] = InBuff
      V[32:33] = global_load_addr
    Compiler allocate new vgprs (V16~V49)to do global load
    V8 is not used during fft calculation
    At the end of the kernel, V8 still holds the value of me*1
    Compiler could use V8 to calculate global write address
      S[0:1] = OutBuff
      S[2:3] = stride_out
      V[0:1] = global_store_addr
      V[8:9] = (0+me*1+0) * stride_out
reason

## Slide 6: Weekly
Solution 1: Cheat compiler
  Use different formula to calculate input/output address.
    addr_in = inOffset + ( 0 + me*1 + 0 + instr_step) * stride_in;
    addr_out = outOffset + ( 0 + me*1 + 0 + (instr_step + 1)) * stride_out – stride_out;
  Compiler won’t reserve vgprs for to hold template variable
  Compiler will allocate fewer vgpr for global load
  Vgprs will be re-used during fft calculation
    16 data (32 VGPR)
    Twiddle (12 VGPR)
    Addressing (8 VGPR)
Solution 1

## Slide 7: Weekly
Solution 1: Cheat compiler
Solution 1

## Slide 8: Weekly
Disadvantage
  Because template variable need to re-calculate during global write, compiler will generate more instruction for output address.
  Increase 4 instructions per address, totally 64 instructions
  This will cause perf-drop for small batch size (parallel group less than 4 per CU)
Solution 1

## Slide 9: Weekly
Solution 2: compiler attribute
  Use attribute for fft_op_kernel to limited vgpr usage
    __attribute__((amdgpu_num_vgpr(64)))
  Compiler could only use 64 vgprs at most.
  How the compiler save the 4 vgprs???
  NOT figure out yet (on going)
  How to set the limit number???
Solution 2

## Slide 10: Weekly
Dangerous
  If limit the vgpr to a not reasonable small number,
  the compiler won’t have enough vgprs to do it’s work, it will use scratch buffer.
  That will generate numbers of global memory read/write instructions
  Cause sharply perf-drop
    Amdgpu_vgpr_num(16)
    Duration 0.033ms -> 0.35ms
Solution 2

## Slide 11: Weekly
DANGEROUS
  FFT: length = 3125, dim = 1d, c2c forward, batch size = 300, iteration = 1000
  GPU: 60 CU
  Workload: group size = 125(2 wave), group num = 300, LDS usage = 3125 DW (5 groups per CU at most)
  Origin: VGPR = 120, parallel wave per SIMD = 2, parallel group per CU = 4, dispatch number = 2
  Limit : VGPR = 84, parallel wave per SIMD = 3, parallel group per CU = 5, dispatch number = 1
  Performance drop: duration from 0.064ms to 0.144ms
Solution 2

## Slide 12: Weekly
DANGEROUS
  FFT: length = 3125, dim = 1d, c2c forward, batch size = 300, iteration = 1000
Solution 2
84 VGPR
120 VGPR
second dispatch

## Slide 13: Weekly
DANGEROUS
  FFT: length = 3125, dim = 1d, c2c forward, batch size = 300, iteration = 1000
Solution 2
84 VGPR
120 VGPR
scratch memory access

## Slide 14: Weekly
Performance
  FFT: length = 4096, dim = 1d, c2c forward, batch size = 240, iteration = 1000
  GPU: 60CU
  Workload: group size = 256(4wave), group num = 240, LDS usage = 4K DW
performance
VGPR | Parallel wave / SIMD | Parallel group / CU | Dispatch times | Duration (ms)
52 | 4 | 4 | 1 | 0.032
64 | 4 | 4 | 1 | 0.033
68 | 3 | 3 | 2 | 0.035
  for multi-batch, increase parallel wave/group number will reduce dispatch times
  reduce vgpr usage will increase instruction number

## Slide 15: Weekly
performance
52 VGPR
64 VGPR
68 VGPR
second dispatch

## Slide 16: Weekly
performance
52 VGPR
64 VGPR
68 VGPR
second dispatch