## Slide 1: rocprof
Has-trace

## Slide 2: rocprof
Prof 3 dim rocfft
  6 kernels:
Has-trace
 | Forward | Durations(ns) | withonly | without
1 | fft_fwd_ip_len50 | 27,200 | 0.079ms | 0.178ms
2 | real_post_process | 31,840 | 0.083ms -> 0.073ms | 0.192ms
3 | fft_fwd_ip_len100 | 34,240 | 0.085ms | 0.174ms
4 | transpose_kernel2 | 23,360 | 0.101ms | 0.184ms
5 | fft_fwd_op_len100 | 33,920 | 0.089ms | 0.177ms
6 | transpose_kernel2 | 24,000 | - | -
 | Launch kernel | 56,000 | 0.056ms | 
 | total | 0.216ms |  | 

## Slide 3: Weekly
 | Client Forward | Client Backward | Rocfft-rider fwd | Rocfft-rider bwd
09/11 | 0.324ms | 0.325ms |  | 
09/18 | 0.216ms | 0.216ms | 0.2926ms | 0.319ms
10/22 | 0.206ms |  |  | 
 | LDSBankConflict |  | MemUnitStalled | 
 | before | after | before | after
real_post_process_kernel_transpose | 24% | 0% | 19% | 10%
transpose_kernel2_scheme |  | 14% |  | 3%

## Slide 4: ttrace
Fft_fwd_ip_len50

## Slide 5: ttrace
Real_post_process_kernel_transpose

## Slide 6: ttrace
Fft_fwd_ip_len100

## Slide 7: ttrace
transpose_kernel2_schemeI

## Slide 8: Perf counter
Origin data

## Slide 9: Perf counter
Busy time
For transpose kernel，memory busy > alu busy
For fft kernel, memory busy = alu busy
Memory limitation

## Slide 10: Perf counter
Issue instruction
Compare with pre-slides
  Fft kernel issue 5%~6% mem instr, but cost 26%~28% gpu time
  Transpose kernel issue 10% mem instr, cost 20% gpu time
  Real post kernel issue 10% mem instr, cost 46% gpu time

## Slide 11: Perf counter
Lds bank conflict
Real_post_process_kernel: 24% lds time is conflict
For transpose kenrel: 15% LDS time is conflict

## Slide 12: Perf counter
L2 hit rate
First 2 fft kernel has high hit rate (50%), while 3rd fft kernel has low hit rate (26%) ?

## Slide 13: Perf counter
coalescing
All kernel have very good coalescing practice (cacheline usage 100%)

## Slide 14: Perf counter
Mem stall
Real post kernel and fft100 kernel has above 10% stall time(channel conflict)

## Slide 15: Perf counter
transpose
Tile transpose
  Group size = 64 * 16
  Tile = 64 * 64 float2
  Transpose one tile per group
  Process 4 float2 per thread
  Bandwidth = 316.64GB/s vs 1024GB/s

## Slide 16: Perf counter
transpose
LDS usage
  4096 float2 (32KB) per group
  Write to lds has bank conflict
    SQ_INSTS_LDS (18200)
    SQ_WAIT_INST_LDS (412915)
    SQ_LDS_BANK_CONFLICT (474300)
    LDSBankConflict (16%)

## Slide 17: Perf counter
transpose
Reduce bank conflict with padding
  Pad one float2 every row (64 float2)
    SQ_INSTS_LDS (18200)
    SQ_WAIT_INST_LDS (926)
    SQ_LDS_BANK_CONFLICT (0)
    LDSBankConflict (0%)

## Slide 18: Perf counter
transpose
Reduce bank conflict with padding
  Increase workgroup number
  Improve only less than 200 clk

## Slide 19: Perf counter
transpose
Reduce instruction

## Slide 20: Perf counter
transpose
Reduce instruction
  6salu + 9valu + 3branch  1salu + 8valu + 1branch
  196 clk  92 clk

## Slide 21: Perf counter
transpose
L1 access
  Pattern
    Each lane (16 threads) access one cacheline
    Each wave (64 threads) access 4 entire cacheline

## Slide 22: Perf counter
transpose
L2 access
  Pattern
    Each wave (64 threads) access 2 entire channel
    No channel conflict
    Transpose kernel has 3% memory stall.

## Slide 23: Perf counter
Realcomplex_even_transpose
Tile transpose
  n = 50, m = 100, dim = 3
  group size = [16, 16, 1]
  grid size = [2, 700, 1]
  Tile = 16 * 16 float2
    Len0 = 50
    Tile_size = 16
  Transpose one tile per group
  Process 4 float2 per thread
  Bandwidth = 316.64GB/s vs 1024GB/s